#### Table 1 - G-Code Commands for Turning and Milling Operations
Code	Turning	Milling
G00	Fast move	Fast move
G01	Linear interpolation	Linear interpolation
G02	Circular Interpolation CW	Circular Interpolation CW
G03	Circular interpolation CCW	Circular interpolation CCW
G04	Dwell	Dwell
G09	Exact stop check	Exact stop check
G10	Data setting	Data setting
G11	Data setting cancel	Data setting cancel
G15	—	Polar coordinates
G16	—	Polar coordinates cancel
G17	—	XY plane designate
G18	—	ZX plane designate
G19	—	YZ plane designate
G20	Set English units	Set English units
G21	Set metric units	Set metric units
G22	Stored stroke check on	Stored stroke check on
G23	Stored stroke check off	Stored stroke check off
G25	Spindle speed fluctuation detect on	Spindle speed fluctuation detect on
G26	Spindle speed fluctuation detect off	Spindle speed fluctuation detect off
G27	Machine zero position check	Machine zero position check
G28	Machine zero return (point 1)	Machine zero return (point 1)
G29	Return from machine zero	Return from machine zero
G30	Machine zero return (point 2)	Machine zero return (point 2)
G31	Skip function	Skip function
G32	Threading constant lead	—
G35	Circular threading CW	—
G36	Circular threading CCW	—
G40	Tool nose radius offset cancel	Cutter radius offset cancel
G41	Tool nose radius offset left	Cutter radius offset left
G42	Tool nose radius offset right	Cutter radius offset right
G43	—	Tool length offset positive
G44	—	Tool length offset negative
G49	—	Tool length compensation cancel
G50	Maximum rpm preset	Scaling function cancel
G51	—	Scaling function
G52	Local coordinate system set	Local coordinate system set
G53	Machine coordinate system set	Machine coordinate system set
G54	Work coordinate 1	Work coordinate 1
G55	Work coordinate 2	Work coordinate 2
G56	Work coordinate 3	Work coordinate 3
G57	Work coordinate 4	Work coordinate 4
G58	Work coordinate 5	Work coordinate 5
G59	Work coordinate 6	Work coordinate 6
G60	—	Single direction positioning
G61	Exact stop mode	Exact stop mode
G62	Automatic corner override mode	Automatic corner override mode
G63	—	Tapping mode
G64	Cutting mode	Cutting mode
G65	Custom macro call	Custom macro call
G66	Custom modal macro call	Custom macro modal call
G67	Custom modal macro call cancel	Custom modal macro call cancel
G68	Mirror image for double turrets	Coordinate system rotation
G69	Mirror image for double turrets cancel	Coordinate system rotation cancel
G70	Profile finishing cycle	—
G71	Profile roughing cycle Z axis direction	—
G72	Profile roughing cycle X axis direction	—
G73	Pattern repetition cycle	High speed peck drilling cycle
G74	Drilling cycle	Left hand threading cycle
G75	Grooving cycle	—
G76	Threading cycle	Fine boring cycle
G80	—	Fixed cycle cancel
G81	—	Drilling cycle
G82	—	Spot drilling cycle
G83	—	Peck drilling cycle
G84	—	Right hand threading cycle
G85	—	Boring cycle
G86	—	Boring cycle
G87	—	Back boring cycle
G88	—	Boring cycle
G89	—	Boring cycle
G90	Cutting cycle AA /Absolute commandB	Absolute command
G91	Incremental commandB	Incremental command
G92	Tool position registerB	Tool position register
G94	Feed rate per minuteB	—
G95	Feed rate per revolutionB	—
G96	Constant surface speed	—
G97	Constant spindle speed	—
G98	Feed rate per minuteA	Return to initial level in a fixed cycle
G99	Feed rate per revolutionA	Return to R level in a fixed cycle

#### Table 1 - M-Codes Commands Summary for Lathe Operations
Note: *Based on Fanuc controller codes
M code*	Description*
M00	Program stop
M01	Optional program stop
M02	End of program
M03	Spindle start forward CW
M04	Spindle start reverse CCW
M05	Spindle stop
M08	Coolant on
M09	Coolant off
M29	Rigid tap mode
M30	End of program reset
M40	Spindle gear at middle
M41	Low Gear Select
M42	High Gear Select
M68	Hydraulic chuck close
M69	Hydraulic chuck open
M78	Tailstock advancing
M79	Tailstock reversing
M94	Mirrorimage cancel
M95	Mirrorimage of X axis
M98	Subprogram call
M99	End of subprogram

Table data source: http://www.helmancnc.com/fanuc-m-code-list/
#### Table 2 - M-Codes Command Summary for Milling Operations
M code*	Description*
M00	Program stop
M01	Optional program stop
M02	End of program
M03	Spindle start forward CW
M04	Spindle start reverse CCW
M05	Spindle stop
M06	Tool change
M07	Coolant ON – Mist coolant/Coolant thru spindle
M08	Coolant ON – Flood coolant
M09	Coolant OFF
M19	Spindle orientation
M28	Return to origin
M29	Rigid tap
M30	End of program (Reset)
M41	Low gear select
M42	High gear select
M94	Cancel mirrorimage
M95	Mirrorimage of X axis
M96	Mirrorimage of Y axis
M98	Subprogram call
M99	End of subprogram